## Slide 1: HDL Part III
陳培殷
國立成功大學 資訊工程系

## Slide 2
Parameterized Design (1/2)
module test (a , b , c);
parameter width = 8;
input [width - 1 : 0] a, b;
output [width - 1 : 0] c;
assign c = a & b;
endmodule
module PARAM(A , B , C);
input [7 : 0] A , B;
output [7 : 0] C;
wire f;
or o1(f,A,B);
test #(4) u1(A , f , C);
endmodule
Save the file as PARAM.v and compile (synthesis) it
the width value become 4
Override the value of width when the test module is instantiated

## Slide 3
Parameterized Design (2/2)
Override those values of many parameters when the test_2 module
is instantiated (width = 5; height = 4; length = 4)
module PARAM_1(A , B , C , D);
input [4 : 0] A;
input [3 : 0] B;
input [3 : 0] C;
output [5 : 0] D;
test_2 #(5 , 4 , 4) u1(A , B , C , D);
endmodule
module test_2(A , B , C , D);
parameter width = 8;
parameter height = 8;
parameter length = 8;
input [width - 1 : 0] A;
input [height - 1 : 0] B;
input [length- 1 : 0] C;
output [width : 0] D;
assign D = A + B + C;
endmodule

## Slide 4: Expressions
An expression comprises of operators and operands, see Example, and are covered separately in the following two sections.
Example
expression
operators
operands
W<= X - Y + Z

## Slide 5: Verilog Operands
Four data objects form the operands of an expression
Verilog Operands
Identifiers Literals string (bit & character) numeric (integer, real+) Function Call Index & Slice Names
Identifiers
Verilog identifiers consists of letters, digits, underscores (_) and dollar sign ($)
Verilog is case sensitive, so upper and lower case identifier names are treated
as different identifiers
34
4’b 1101

## Slide 6: Identifier and Literal Operands (1/2)
Numeric (integer) literal
Bit string literals
Identifier
Identifier
module LITERALS(A1, A2, B1, B2, Y1, Y2);
input A1, A2, B1, B2;
output [7:0] Y1; output [5:0] Y2;
parameter CST = 4’b 1010, TF=25;
reg [7:0] Y1; reg [5:0] Y2;
always @(A1 or A2 or B1 or B2)
begin
if (A1 == 1)
Y1 = {CST, 4’b 0000};
else if (A2 == 1)
Y1 = {CST, 4’b 0101};
else
Y1 = {CST, 4’b 1111};
if (B1 == 0) Y2 = 10;
else if (B2 == 1) Y2 = 15;
else Y2 = TF +10 +15;
end
endmodule

## Slide 7
Index operand specifies a single element of an array and slice operand specifies a sequence of elements within an array
module INDEX_SLICE_NAME (A, B, Y);
input [5:0] A, B;
output [11:0]Y;
parameter C = 3’b111;
reg [11:0] Y;
always @(A or B)
begin
Y[2:0] = A[2:0];
Y[3] = A[3] | B[3];
Y[5:4] = {A[5] | B[5], A[4] & B[4]};
Y[8:6] = B[2:0];
Y[11:9] = C;
end
endmodule
Identifier and Literal Operands (2/2)

## Slide 8: Operators (1/3)
Operators perform an operation on one or more operands within an expression. An expression combines operands with appropriate operators to produce the desired function expression.
Name | Operator
bit-select or part-select parenthesis | [ ] ( )
Arithmetic Operators multiplication division addition subtraction modulus | * / + - %
Sign Operators identity negation | + -

## Slide 9: Operators (2/3)
Name | Operator
Relational Operators less than less than or equal to greater than greater than or equal to | < <= > >=
Equality Operators logic equality logic inequality case equality case inequality | == != === !==
Logical Comparison Operators NOT AND OR | ! && ¦¦
Logical Bit-Wise Operators unary negation NOT binary AND binary OR binary XOR binary XNOR | ~ & ¦ ^ ^~ or ~^

## Slide 10: Operators (3/3)
Name | Operator
Shift Operators logical shift left logical shift right | << >>
Concatenation & Replication Operators concatenation replication | { } {{ }}
Reduction Operators AND OR NAND NOR XOR XNOR | & ¦ ~& ~¦ ^ ^~ or ~^
Conditional Operator conditional | ?:

## Slide 11: Arithmetic Operators
Arithmetic operators:
+
-
*
/ (++)non-syn.
% (++)non-syn.
A[2:0] | 000 | 001 | 101 | 110
B[2:0] | 101 | 111 | 100 | 001
Y1[3:0] | 0101 | 1000 | 1001 | 0111
Y2[3:0] | 1011 (-5) | 1010(-6) | 0001(+1) | 0101(+5)
Y3[4:0] | 00000 | 00111 | 10100 | 00110
(不建議)
module ARITHMETIC(A, B, Y1, Y2, Y3);
input [2:0] A, B;
output [3:0] Y1;
output [4:0] Y3;
output [3:0] Y2;
reg [3:0] Y1;
reg [4:0] Y3;
reg [3:0] Y2;
always @(A or B)
begin
Y1 = A + B;
Y2 = A - B;
Y3 = A * B;
Y4 = A / B;
Y5 = A % B;
end
endmodule

## Slide 12: Relational Operators
module RELATIONAL_OPERATORS(A, B, Y);
input [2:0] A;
input [2:0] B;
output [3:0] Y;
reg [3:0] Y;
always @(A or B)
begin
Y[0] = A > B;
Y[1] = A >= B;
Y[2] = A < B;
if ( A <= B)
Y[3] = 1;
else
Y[3] = 0;
end
endmodule
Relational operators:
<
<=
>=
>
A[2:0] | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 3 | 0
B[2:0] | 3 | 5 | 6 | 7 | 2 | 1 | 0 | 3 | 6
Y[3] | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
Y[2] | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1
Y[1] | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
Y[0] | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0

## Slide 13: Shift Operators
module SHIFT(A, Y1, Y2);
input [7:0] A;
output [7:0] Y1;
output [7:0] Y2;
reg [7:0] Y1;
reg [7:0] Y2;
parameter B=3;
always @(A)
begin
Y1 = A << B;
Y2 = A >> 2;
end
endmodule
Shift operators:
(1) << (left shift)
(2) >> (right shift)
A[7:0] | 00000000 | 00000001 | 00000011 | 00000100
Y1[7:0] | 00000000 | 00001000 | 00011000 | 00100000
Y2[7:0] | 00000000 | 00000000 | 00000000 | 00000001

## Slide 14: Concatenation & Replication Operators
module CONCATENATION (A, B, Y);
input [2:0] A;
input [2:0] B;
output [14:0] Y;
reg [14:0] Y;
parameter C=3’b011;
always @(A)
begin
Y = { B, A, { 2 { C } }, 3’b 001};
end
endmodule
Concatenation {}
Replication {{}}
A[2:0] | 000 | 001 | 010 | 011
B[2:0] | 000 | 010 | 100 | 110
Y[14:0] | 000000011011001 | 010001011011001 | 100010011011001 | 110011011011001
3+3+2*3+3=15

## Slide 15: Conditional Operators
module ADD_SUB (A, B, SEL, Y);
input [7:0] A; input [7:0] B;
input SEL;
output [8:0] Y1,Y2;
reg [8:0] Y2,Y1;
always @( A or B)
begin
Y1 = ( SEL == 1 ) ? A + B : A – B ;
Y2 = (!SEL) ? A : B;
end
endmodule
Conditional operators:
? :
SEL | 0 | 0 | 1 | 1
A[7:0] | 00000100 | 00000001 | 00000100 | 00000001
B[7:0] | 00000001 | 00000010 | 00000001 | 00000010
Y1[8:0] | 00000011 | 11111111 | 00000101 | 00000011
Y2[8:0] | 00000100 | 00000001 | 00000001 | 00000010
true false

## Slide 16
3 to 8 Decoder (1/4)
E | In[2] | In[1] | In[0] | Out[7] | Out[6] | Out[5] | Out[4] | Out[3] | Out[2] | Out[1] | Out[0]
0 1 1 1 1 1 1 1 1 | X 0 0 0 0 1 1 1 1 | X 0 0 1 1 0 0 1 1 | X 0 1 0 1 0 1 0 1 | 0 0 0 0 0 0 0 0 1 | 0 0 0 0 0 0 0 1 0 | 0 0 0 0 0 0 1 0 0 | 0 0 0 0 0 1 0 0 0 | 0 0 0 0 1 0 0 0 0 | 0 0 0 1 0 0 0 0 0 | 0 0 1 0 0 0 0 0 0 | 0 1 0 0 0 0 0 0 0
3-8
decoder
In[0]
In[0]
In[2]
E
Out[0]
Out[7]
.
.

## Slide 17
3 to 8 Decoder (2/4)
In[2]
In[1]
In[0]
E
Out[0]
Out[1]
Out[2]
Out[3]
Out[4]
Out[5]
Out[6]
Out[7]
Structural description
module decoder (E , In , Out);
input E; input [2:0] In;
output [7:0] Out;
wire [7:0] Out;
wire tmp0 , tmp1 , tmp2;
not not1(tmp0,In[0]); not not2(tmp1,In[1]);
not not3(tmp2,In[2]);
and and0(Out[0] , E , tmp0 , tmp1 , tmp2);
and and1(Out[1] , E , In[0] , tmp1 , tmp2);
and and2(Out[2] , E , tmp0 , In[1] , tmp2);
and and3(Out[3] , E , In[0] , In[1] , tmp2);
and and4(Out[4] , E , tmp0 , tmp1 , In[2]);
and and5(Out[5] , E , In[0] , tmp1 , In[2]);
and and6(Out[6] , E , tmp0 , In[1] , In[2]);
and and7(Out[7] , E , In[0] , In[1] , In[2]);
endmodule

## Slide 18
3 to 8 Decoder (3/4)
Data flow description
module decoder(E , In , Out);
input E;
input [2:0]In;
output [7:0]Out;
wire [7:0]Out;
assign Out = E ? 1'b1 << In : 8'h0;
endmodule
In[2]
In[1]
In[0]
E
Out[0]
Out[1]
Out[2]
Out[3]
Out[4]
Out[5]
Out[6]
Out[7]
Synthesized and
optimized by tools
true false

## Slide 19
3 to 8 Decoder (4/4)
Behavioral description
module Decoder_Behavioral(E, In, Out);
  Input E;
  input [2:0] In;
  output [7:0] Out;
  reg [7:0] Out;
  always @(E or In)
  begin
  if(!E)
  Out = 8'h00;
  else
  begin
  case(In)
  3'b000: Out = 8'h01;
  3'b001: Out = 8'h02;
  3'b010: Out = 8'h04;
  3'b011: Out = 8'h08;
  3'b100: Out = 8'h10;
  3'b101: Out = 8'h20;
  3'b110: Out = 8'h40;
  default: Out = 8'h80;
  endcase
  end
  end
  endmodule
0 X X X 0 0 0 0 0 0 0 0
1 0 0 0 0 0 0 0 0 0 0 1
1 0 0 1 0 0 0 0 0 0 1 0
1 0 1 0 0 0 0 0 0 1 0 0
1 0 1 1 0 0 0 0 1 0 0 0
1 1 0 0 0 0 0 1 0 0 0 0
1 1 0 1 0 0 1 0 0 0 0 0
1 1 1 0 0 1 0 0 0 0 0 0
1 1 1 1 1 0 0 0 0 0 0 0
E
Out
In

## Slide 20
Hierarchical Design of 3-8 decoder
module decoder_2_4(E , In , Out);
input E; input [1:0] In;
output [3:0]Out; wire [3:0] Out;
assign Out = E ? 1'b1 << In : 4'h0;
endmodule
module decode_3_8(E , In , Out);
input E; input [2:0] In;
output [7:0] Out; wire E1 , G1 , G2;
not u1(E1 , In[2]); and a1(G1 , E , In[2]);
and a2(G2 , E , E1);
decoder_2_4 M(G1 , In[1 : 0] , Out[7 : 4]);
decoder_2_4 L(G2 , In[1 : 0] , Out[3 : 0]);
endmodule
2 to 4 decoder
G1
Decoder1
2- 4 decoder
G2
Out[7:4]
Out[3:0]
E
In[0]
In[1]
In[2]
E1
In[0]
In[1]
In[0]
In[1]
Decoder 0
2- 4 decoder