## Slide 1: HDL Part VII
陳培殷
國立成功大學 資訊工程系

## Slide 2
Modern Design (1/2)
Modern design is composed of (1) Datapath and
(Note)
Control
unit
Datapath
Control
signals
Status
signals
Datapath
outputs
Control
outputs
Datapath
inputs
Control
inputs
(2) Controller (control unit or control path)

## Slide 3
C: Combinational circuit
S: Sequential circuit
C
Register-transfer-level block diagram
Modern Design (2/2)
C
C
C
S
S
S
C
Control Unit
D
Q
D
Q
.
.
Datapath

## Slide 4
Optimization for RTL Design
Optimization for control unit:
1. As suggestion by most textbooks
of “Logic System Design”
2. Write a good-style HDL descriptions
which are optimized by EDA tools

## Slide 5
Design description or
timing diagram
Optimization for Control Unit
Develop
state diagram
Develop next-state
and output tables
Minimize states
Encode input, states,
and outputs
Derive
excitation equation
Optimize
logic circuit
Derive logic schematic
and timing diagram
Simulation
Functional verification
and timing analysis
Traditional optimization
flow for control unit
Control Unit
Finite State Machine
(FSM)
Decide the
memory elements

## Slide 6
Finite State Machine (1/4)
Moore machine: (output is dependent only on current state)
Mealy machine: (output is dependent on input and state)
State diagram
S0
S2
S1
S3
0/0
1/1
1/1
1/0
0/0
0/1
0/0
1/1
Four states: S0, S1, S2, S3
Input/Output
Input/Output
Present State | Next State |  | Output | 
 | I=0 | I=1 | I=0 | I=1
S0 | S0 | S1 | 0 | 1
S1 | S1 | S2 | 1 | 0
S2 | S2 | S0 | 0 | 1
S3 | S3 | S1 | 0 | 1
Initial state
Next-state and output tables (I=input)
A mealy machine

## Slide 7
Finite State Machine (2/4)
Next State Logic
(combinational)
Current State Register
(sequential)
Output Logic
(combinational)
clock
inputs
asynchronous reset
Moore
output
Moore Machine (state-based machine)
Next State Logic
(combinational)
Current State Register
(sequential)
Output Logic
(combinational)
clock
inputs
asynchronous reset
Mealy
output
Mealy Machine (input-based machine)

## Slide 8
Finite State Machine (3/4)
For best legibility, describe FSM using two or three always@ statements
  (1) current state or state register (sequential circuit)
  (2) next state logic (combinational circuit)
  (3) output logic (combinational circuit)
    Two combinational logic can be merged
Use parameter to describe the state name
ST0
ST1
ST2
ST3
Reset
Y=1
Y=2
Y=4
Control=0
Control=1
Y=3

## Slide 9
Finite State Machine (4/4)
module FSM(Clock, Reset, Control, Y)
input Clock, Reset, Control;
output [2:0] Y;
reg [1:0] CurrentState, Nextstate;
reg [2:0] Y;
parameter [1:0] ST0 = 2’b00,
ST1 = 2’b01,
ST2 = 2’b10,
ST3 = 2’b11;
always @(posedge Clock or posedge Reset)
if (Reset)
CurrentState <= ST0;
else
CurrentState <= NextState;
always @(Control or Currentstate)
begin
NextState = ST0;
case (CurrentState)
ST0: NextState <= ST1;
ST1: if (Control)
NextState <= ST2;
else
NextState <= ST3;
ST2: NextState <= ST3;
ST3: NextState <= ST0;
endcase end
always @(CurrentState)
begin
case(CurrentState)
ST0: Y <= 1; ST1: Y <= 2;
ST2: Y <= 3; ST3: Y <= 4;
endcase
end endmodule
State name
(parameter)
State
register
(Seq.C.)
Next state
logic
(Comb.C.)
Output
logic
(Comb.C.)
ST0
ST1
ST2
ST3
Reset
Y=1
Y=2
Y=4
Control=0
Control=1
Y=3

## Slide 10
Moore Machine (1/2)
Present State | Next State |  | Output | 
 | I=0 | I=1 | I=0 | I=1
S0 | S0 | S2 | 0 | 0
S1 | S0 | S2 | 1 | 1
S2 | S2 | S3 | 1 | 1
S3 | S3 | S1 | 0 | 0
Next-state and output tables (I=input)
Design description or
timing diagram
Develop
state diagram
Develop next-state
and output tables
Minimize states
Encode input, states,
and outputs
Decide the
memory elements
Derive
excitation equation
Optimize
logic circuit
Derive logic schematic
and timing diagram
Simulation
Functional verification
and timing analysis
Optimization flow
S0
S1
S2
S3
0/0
1/0
0/1
0/0
0/1
1/0
1/1
1/1

## Slide 11
Note: This is a good-style HDL (only “State” is implemented with flip-flops)
module moore_good(Clk,
Reset, In_Data, Out_Data);
input Clk, Reset, In_Data;
output [1:0] Out_Data;
reg [1:0] Out_Data;
reg [1:0] State, NextState;
parameter S0=2'b00, S1=2'b01,
S2=2'b10, S3=2'b11;
always @(posedge Clk or
posedge Reset)
begin
if(Reset)
State = S0;
else
State = NextState;
end
always @(In_Data or State)
begin
case(State)
S0: begin
if(In_Data == 1)
NextState = S2;
else
NextState = S0;
end
S1:begin
if(In_Data == 1)
NextState = S2;
else
NextState = S0;
end
S2: begin
if(In_Data == 1)
NextState = S3;
else
NextState = S2;
end
S3: begin
if(In_Data == 1)
NextState = S1;
else
NextState = S3;
end
endcase
end
always @(State)
begin
case(State)
S0:Out_Data = 0;
S1:Out_Data = 1;
S2:Out_Data = 1;
S3:Out_Data = 0;
endcase
end
endmodule
Output logic
State register (flip-flops)
Next state logic
Moore Machine (2/2)
Present State | Next State |  | Output | 
 | I=0 | I=1 | I=0 | I=1
S0 | S0 | S2 | 0 | 0
S1 | S0 | S2 | 1 | 1
S2 | S2 | S3 | 1 | 1
S3 | S3 | S1 | 0 | 0

## Slide 12
Traffic Light Controller (1/6)
Control Unit
Datapath
Counter
Comparator
Red
Green
Yellow
Next
State
Logic
Output
Logic
State Registers
Seq.
Comb.
Comb.
Recount_counter
R
Y
G
1/100
1/010
1/001
0/100
0/010
0/001
Recount_Counter16/Red Green Yellow
Input/Output
Rt Gt Yt
Current_times
Recount_counter
4 2 0
R_time: 4+1=5 cycles
G_time: 2+1=3 cycles
Y_time: 0+1=1 cycles

## Slide 13
Traffic Light Controller (2/6)
module traffic(Clock,Reset,Red,Green,Yellow);
input Clock,Reset; output Red,Green,Yellow;
wire Recount_conter; wire [3:0] Counter_Number;
Traffic_Control (.Clock(Clock),.Reset(Reset),
.Recount_Counter16(Recount_conter),.Red(Red),
.Green(Green),.Yellow(Yellow));
Datapath (.Clock(Clock), .Reset(Reset), .RGY({Red,Green,Yellow}),
.Recount(Recount_conter));
endmodule
module Datapath(Clock, Reset, RGY, Recount);
input Clock, Reset; input [2:0] RGY;
output Recount; wire [3:0] Counter_Number;
Compare A1(.current_times(Counter_Number), .RGY(RGY),
.Recount_conter16(Recount));
Counter16 A2(.Clock(Clock),.Reset(Reset),
.Recount_Counter16(Recount),.Count_Out(Counter_Number));
endmodule

## Slide 14
Traffic Light Controller (3/6)
module Counter16(Clock,Reset,Recount_Counter16,
Count_Out);
input Clock,Reset,Recount_Counter16;
output [3:0] Count_Out;
reg [3:0] Count_Out;
always@(posedge Clock)
begin
if(Reset)
Count_Out=0;
else
begin
if(Recount_Counter16)
Count_Out=0;
else
Count_Out=Count_Out+1;
end
end
endmodule

## Slide 15
Traffic Light Controller (4/6)
module compare(current_times,
RGY, Recount_conter16);
input [2:0] RGY;
input [3:0] current_times;
output Recount_conter16;
reg Recount_conter16;
parameter R_times=4, G_times=2,
Y_times=0;
always @(RGY)
begin
case(RGY)
3’b100:begin
if(current_times ==R_times)
Recount_conter16=1;
else
Recount_conter16=0;
end
3’b001:begin
if(current_times ==Y_times)
Recount_conter16=1;
else
Recount_conter16=0;
end
3’b010:begin
if(current_times ==G_times)
Recount_conter16=1;
else
Recount_conter16=0;
end
default: Recount_conter16=1;
endcase
end
endmodule

## Slide 16
Traffic Light Controller (5/6)
State Register (Seq. C.)
Next State Logic (Comb. C.)
module Traffic_Control(Clock,Reset,
Recount_Counter16,Red,Green,Yellow);
input Clock, Reset,Recount_Counter16;
output Red, Green, Yellow;
reg Red, Green, Yellow;
reg [1:0] currentstate,nextstate;
parameter [1:0] Red_Light=0, Green_Light=1,
Yellow_Light=2;
always@(posedge Clock)
begin
if(Reset)
currentstate = Red_Light;
else
currentstate = nextstate;
end
always@(currentstate)
begin
case(currentstate)
Red_Light:begin
if(Recount_Counter16)
nextstate=Green_Light;
else
nextstate=Red_Light; end
Green_Light:begin
if(Recount_Counter16)
nextstate=Yellow_Light;
else
nextstate=Green_Light; end
Yellow_Light:begin
if(Recount_Counter16)
nextstate=Red_Light;
else
nextstate=Yellow_Light; end
default: nextstate=Red_Light;
endcase
end

## Slide 17
Traffic Light Controller (6/6)
Output Logic (Comb. C.)
always @(currentstate)
begin
case(currentstate)
Red_Light:begin
Red=1'b1;
Green=1'b0;
Yellow=1'b0;
end
Green_Light:begin
Red=1'b0;
Green=1'b1;
Yellow=1'b0;
end
Yellow_Light:begin
Red=1'b0;
Green=1'b0;
Yellow=1'b1;
end
default:begin
Red=1'b0;
Green=1'b0;
Yellow=1'b0;
end
endcase
end
endmodule